## Slide 1: Engr. Dr. Muhammad Nadeem Majeed
PhD Computer Engineering
MS Computer Engineering
Certifications:
      Project Management Professional (PMP)®
      PRINCE2 Agile Practitioner
      Professional Scrum Master (PSM)
      Certified Lean Six Sigma Green Belt (CSSC)
      ITIL Certified
      Cisco Certified Network Associate (CCNA)
      Juniper Networks Certified Internet Associate (JNCIA)
      IBM Certified Data Engineer
Experience: 21 Years of Teaching & Network Management
University of The Punjab, Lahore
University of Engineering and Technology Taxila.
NUST School of Electrical Engineering and Computer Science. Islamabad.
University of Arid Agriculture Rawalpindi.
Research interests:
Mispronunciation Detection,
Disease classification.
Network and Communications.
Machine Learning
Associate Professor
Department of Data Science

## Slide 2
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Contact info:
nadeem.majeed@pucit.edu.pk
0333-1049181
Department of Data Science,
University of the Punjab, Lahore
Computer Networks Introduction
Part-01
Dr. Muhammad Nadeem Majeed
Notes: Version History
7.2 (January 2020)
All slides reformatted for 16:9 aspect ratio
Use of Calibri font, rather that Gill Sans MT
Updated slide content for 2020 link technologies and applications
Add more animation throughout
New Master slide
Feb. 2020 (8.0)
a few updates suggest by Catherine Rosenberg (thanks!)
titles in a lighter font
Sept 2020 (8.1)
Added ~7 new slides, in particular: data center slide; routing versus forwarding; security line of defense; several on encapsulation and layers (this section is a lot better now). Other relative minor changes throughout

## Slide 3: introduction
Goal:
Get “feel,” “big picture,” introduction to terminology
  more depth, detail later in course
Overview/roadmap:
What is the Internet? What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Protocol layers, service models
Security
History

## Slide 4: The Internet: a “nuts and bolts” view
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches: forward packets (chunks of data)
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  hosts = end systems
  running network apps at Internet’s “edge”
Networks
  collection of devices, routers, links: managed by an organization

## Slide 5: “Fun” Internet-connected devices
Web-enabled toaster +
weather forecaster
Internet phones
Slingbox: remote
control cable TV
Security Camera
IP picture frame
Internet
refrigerator
Tweet-a-watt:
monitor energy use
sensorized,
bed
mattress
Amazon Echo
Others?
Pacemaker & Monitor
AR devices
Fitbit
Gaming devices
cars
scooters
bikes

## Slide 6: The Internet: a “nuts and bolts” view
Internet: “network of networks”
  Interconnected ISPs
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
protocols are everywhere
  control sending, receiving of messages
  e.g., HTTP (Web), streaming video, Skype, TCP, IP, WiFi, 4G, Ethernet
Ethernet
HTTP
Skype
IP
WiFi
4G
TCP
Streaming
video
Internet standards
  RFC: Request for Comments
  IETF: Internet Engineering Task Force

## Slide 7: The Internet: a “services” view
Infrastructure that provides services to applications:
  Web, streaming video, multimedia teleconferencing, email, games, e-commerce, social media, inter-connected appliances, …
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
HTTP
Skype
Streaming
video
provides programming interface to distributed applications:
  “hooks” allowing sending/receiving apps to “connect” to, use Internet transport service
  provides service options, analogous to postal service

## Slide 8: What’s a protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on message transmission, receipt
Rules for:
… specific messages sent
… specific actions taken when message received, or other events

## Slide 9: What’s a protocol?
A human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET http://gaia.cs.umass.edu/kurose_ross
Notes: Explain important points
distributed entities, exchanging messages (governed by protocols)
Time going down
go over definition of protocol (showing format, order of messages sent and received, and actions taken)
We’ll see these kinds of diagrams a lot

## Slide 10: Roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 11: A closer look at Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
hosts: clients and servers
servers often in data centers

## Slide 12: A closer look at Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links

## Slide 13: A closer look at Internet structure
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links
Network core:
  interconnected routers
  network of networks
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 14: Access networks and physical media
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks (WiFi, 4G/5G)

## Slide 15: Access networks: cable-based access
cable
modem
splitter
…
cable headend
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
frequency division multiplexing (FDM): different channels transmitted in different frequency bands

## Slide 16: Access networks: cable-based access
cable
modem
splitter
…
cable headend
data, TV transmitted at different
frequencies over shared cable
distribution network
HFC: hybrid fiber coax
  asymmetric: up to 40 Mbps – 1.2 Gbps downstream transmission rate, 30-100 Mbps upstream transmission rate
network of cable, fiber attaches homes to ISP router
  homes share access network to cable headend
cable modem
termination system
CMTS
ISP

## Slide 17: Access networks: digital subscriber line (DSL)
ISP
central office
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
  use existing telephone line to central office DSLAM
    data over DSL phone line goes to Internet
    voice over DSL phone line goes to telephone net
  24-52 Mbps dedicated downstream transmission rate
  3.5-16 Mbps dedicated upstream transmission rate
DSL
modem
splitter
DSL access
multiplexer

## Slide 18: Access networks: home networks
to/from headend or central office
cable or DSL modem
router, firewall, NAT
wired Ethernet (1 Gbps)
WiFi wireless access
point (54, 450 Mbps)
Wireless and wired
devices
often combined
in single box

## Slide 19: Wireless access networks
Shared wireless access network connects end system to router
via base station aka “access point”
Wireless local area networks (WLANs)
  typically within or around building (~100 ft)
  802.11b/g/n (WiFi): 11, 54, 450 Mbps transmission rate
to Internet
to Internet
Wide-area cellular access networks
  provided by mobile, cellular network operator (10’s km)
  10’s Mbps
  4G cellular networks (5G coming)

## Slide 20: Access networks: enterprise networks
companies, universities, etc.
  mix of wired, wireless link technologies, connecting a mix of switches and routers (we’ll cover differences shortly)
    Ethernet: wired access at 100Mbps, 1Gbps, 10Gbps
    WiFi: wireless access points at 11, 54, 450 Mbps
Ethernet
switch
institutional mail,
web servers
institutional router
Enterprise link to
ISP (Internet)

## Slide 21: Access networks: data center networks
high-bandwidth links (10s to 100s Gbps) connect hundreds to thousands of servers together, and to Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Courtesy: Massachusetts Green High Performance Computing Center (mghpcc.org)

## Slide 22: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=

## Slide 23: Links: physical media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
Twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps Ethernet

## Slide 24: Links: physical media
Coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple frequency channels on cable
  100’s Mbps per channel
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (10’s-100’s Gbps)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise

## Slide 25: Links: physical media
Wireless radio
signal carried in various “bands” in electromagnetic spectrum
no physical “wire”
broadcast, “half-duplex” (sender to receiver)
propagation environment effects:
  reflection
  obstruction by objects
  Interference/noise
Radio link types:
Wireless LAN (WiFi)
  10-100’s Mbps; 10’s of meters
wide-area (e.g., 4G cellular)
  10’s Mbps over ~10 Km
Bluetooth: cable replacement
  short distances, limited rates
terrestrial microwave
  point-to-point; 45 Mbps channels
satellite
  up to 45 Mbps per channel
  270 msec end-end delay

## Slide 26: Roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 27: The network core
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  network forwards packets from one router to the next, across links on path from source to destination
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 28: Two key network-core functions
1
2
3
0111
destination address in arriving
packet’s header
routing algorithm
header value
output link
0100
0101
0111
1001
3
2
2
1
local forwarding table
Forwarding:
aka “switching”
local action: move arriving packets from router’s input link to appropriate router output link
local forwarding table
Routing:
global action: determine source-destination paths taken by packets
routing algorithms
routing algorithm

## Slide 29
routing

## Slide 30
forwarding
forwarding

## Slide 31: Packet-switching: store-and-forward
packet transmission delay: takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
source
R bps
destination
1
2
3
L bits
per packet
R bps
One-hop numerical example:
L = 10 Kbits
R = 100 Mbps
one-hop transmission delay = 0.1 msec

## Slide 32: Packet-switching: queueing
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for transmission over output link
Queueing occurs when work arrives faster than it can be serviced:

## Slide 33: Packet-switching: queueing
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for transmission over output link
Packet queuing and loss: if arrival rate (in bps) to link exceeds transmission rate (bps) of link for some period of time:
packets will queue, waiting to be transmitted on output link
packets can be dropped (lost) if memory (buffer) in router fills up

## Slide 34: Alternative to packet switching: circuit switching
end-end resources allocated to, reserved for “call” between source and destination
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive
commonly used in traditional telephone networks

## Slide 35: Circuit switching: FDM and TDM
frequency
time
frequency
time
4 users
Frequency Division Multiplexing (FDM)
optical, electromagnetic frequencies divided into (narrow) frequency bands
Time Division Multiplexing (TDM)
time divided into slots
each call allocated its own band, can transmit at max rate of that narrow band
each call allocated periodic slot(s), can transmit at maximum rate of (wider) frequency band (only) during its time slot(s)

## Slide 36: Packet switching versus circuit switching
example:
1 Gb/s link
each user:
  100 Mb/s when “active”
  active 10% of time
Q: how many users can use this network under circuit-switching and packet switching?
N
users
1 Gbps link
…..
circuit-switching: 10 users
Q: how did we get value 0.0004?
A: Probability
packet switching: with 35 users, probability > 10 active at same time is less than .0004

## Slide 37: Packet switching versus circuit switching
great for “bursty” data – sometimes has data to send, but at other times not
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss due to buffer overflow
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior with packet-switching?
  “It’s complicated.” We’ll study various techniques that try to make packet switching as “circuit-like” as possible.
Is packet switching a “slam dunk winner”?
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet switching)?

## Slide 38: Internet structure: a “network of networks”
hosts connect to Internet via access Internet Service Providers (ISPs)
access ISPs in turn must be interconnected
    so that any two hosts (anywhere!) can send packets to each other
resulting network of networks is very complex
    evolution driven by economics, national policies
Let’s take a stepwise approach to describe current Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 39: Internet structure: a “network of networks”
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 40: Internet structure: a “network of networks”
…
…
…
…
…
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.

## Slide 41: Internet structure: a “network of networks”
Option: connect each access ISP to one global transit ISP?
Customer and provider ISPs have economic agreement.
global ISP
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 42: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….

## Slide 43: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. who will want to be connected
IXP
peering link
Internet exchange point
IXP

## Slide 44: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPs
IXP
IXP
access
net
access
net
regional ISP
access
net
access
net
access
net

## Slide 45: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users
IXP
IXP
access
net
access
net
access
net
access
net
access
net
Content provider network
regional ISP

## Slide 46: Internet structure: a “network of networks”
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
At “center”: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider networks (e.g., Google, Facebook): private network that connects its data centers to Internet, often bypassing tier-1, regional ISPs
Regional ISP
Regional ISP
Tier 1 ISP
Tier 1 ISP
IXP
Google
IXP
IXP

## Slide 47: Roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 48: How do packet delay and loss occur?
packets queue in router buffers, waiting for turn for transmission
  queue length grows when arrival rate to link (temporarily) exceeds output link capacity
packet loss occurs when memory to hold queued packets fills up
A
B
packet being transmitted (transmission delay)
packets in buffers (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 49: Packet delay: four sources
dproc: nodal processing
check bit errors
determine output link
typically < microsecs
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 50: Packet delay: four sources
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different

## Slide 51: Caravan analogy
car ~ bit; caravan ~ packet; toll service ~ link transmission
toll booth takes 12 sec to service car (bit transmission time)
“propagate” at 100 km/hr
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr) = 1 hr
A: 62 minutes
toll booth
toll booth
(aka link)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
toll booth
toll booth
(aka link)
toll booth

## Slide 52: Caravan analogy
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, first car arrives at second booth; three cars still at first booth

## Slide 53: Packet queueing delay (revisited)
a: average packet arrival rate
L: packet length (bits)
R: link bandwidth (bit transmission rate)
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving is more than can be serviced - average delay infinite!
La/R ~ 0
La/R -> 1
traffic intensity = La/R
average queueing delay
1
service rate of bits
R
arrival rate of bits
L
a
.
:
“traffic
intensity”

## Slide 54: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
3 probes
3 probes
3 probes
  sends three packets that will reach router i on path towards destination (with time-to-live field value of i)
  router i will return packets to sender
  sender measures time interval between transmission and reply

## Slide 55: Real Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
* Do some traceroutes from exotic countries at www.traceroute.org
* means no response (probe lost, router not replying)
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
3 delay measurements
to border1-rt-fa5-1-0.gw.umass.edu
looks like delays decrease! Why?
trans-oceanic link

## Slide 56: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
A
B
packet being transmitted
buffer
(waiting area)
* Check out the Java applet for an interactive animation (on publisher’s website) of queuing and loss
packet arriving to
full buffer is lost
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all

## Slide 57: Throughput
throughput: rate (bits/time unit) at which bits are being sent from sender to receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)

## Slide 58: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 59: Throughput: network scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/

## Slide 60: Roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History
Notes: Segue: from performance to security

## Slide 61: Network security
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!
We now need to think about:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks

## Slide 62: Network security
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!
We now need to think about:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks

## Slide 63: Bad guys: packet interception
packet “sniffing”:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload

## Slide 64: Bad guys: fake identity
IP spoofing: injection of packet with false source address
A
B
C
src:B dest:A payload

## Slide 65: Bad guys: denial of service
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
2. break into hosts around the network (see botnet)
3. send packets to target from compromised hosts

## Slide 66: Lines of defense:
authentication: proving you are who you say you are
  cellular networks provides hardware identity via SIM card; no such hardware assist in traditional Internet
confidentiality: via encryption
integrity checks: digital signatures prevent/detect tampering
access restrictions: password-protected VPNs
firewalls: specialized “middleboxes” in access and core networks:
    off-by-default: filter incoming packets to restrict senders, receivers, applications
    detecting/reacting to DOS attacks

## Slide 67: Roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 68: Protocol “layers” and reference models
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question: is there any hope of organizing structure of network?
and/or our discussion of networks?

## Slide 69: Example: organization of air travel
a series of steps, involving many services
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
How would you define/discuss the system of airline travel?
end-to-end transfer of person plus baggage

## Slide 70: Example: organization of air travel
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
ticketing service
baggage service
gate service
runway service
routing service
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below

## Slide 71: Why layering?
Approach to designing/discussing complex systems:
explicit structure allows identification, relationship of system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change in layer's service implementation: transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system

## Slide 72: Layered Internet protocol stack
application: supporting network applications
  HTTP, IMAP, SMTP, DNS
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
link
application
network
transport
physical
application
transport
network
link
physical

## Slide 73: Services, Layering and Encapsulation
source
transport-layer protocol encapsulates application-layer message, M, with transport layer-layer header Ht to create a transport-layer segment
  Ht used by transport layer protocol to implement its service
application
transport
network
link
physical
destination
application
transport
network
link
physical
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
Application exchanges messages to implement some application service using services of transport layer
M

## Slide 74: Services, Layering and Encapsulation
source
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
network-layer protocol encapsulates transport-layer segment [Ht | M] with network layer-layer header Hn to create a network-layer datagram
  Hn used by network layer protocol to implement its service
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services

## Slide 75: Services, Layering and Encapsulation
source
Ht
M
link-layer protocol encapsulates network datagram [Hn| [Ht |M], with link-layer header Hl to create a link-layer frame
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Link-layer protocol transfers datagram [Hn| [Ht |M] from host to neighboring host, using network-layer services
M
Ht
Hn
Hl
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services

## Slide 76: Services, Layering and Encapsulation
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
Ht
M
M
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
Ht
M
M
message
segment
datagram
frame
M
Ht
Hn
Hl

## Slide 77: Encapsulation: an end-end view
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
source
Ht
Hn
M
segment
Ht
datagram
destination
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
link
physical

## Slide 78: Roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History

## Slide 79: Internet history
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demo
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 80: Internet history
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
late70’s: proprietary architectures: DECnet, SNA, XNA
1979: ARPAnet has 200 nodes
1972-1980: Internetworking, new and proprietary networks
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best-effort service model
  stateless routing
  decentralized control
define today’s Internet architecture

## Slide 81: Internet history
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: CSnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks

## Slide 82: Internet history
early 1990s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990s: commercialization of the Web
late 1990s – 2000s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000s: commercialization, the Web, new applications

## Slide 83: Internet history
  aggressive deployment of broadband home access (10-100’s Mbps)
2008: software-defined networking (SDN)
increasing ubiquity of high-speed wireless access: 4G/5G, WiFi
service providers (Google, FB, Microsoft) create their own networks
    bypass commercial Internet to connect “close” to end user, providing “instantaneous” access to social media, search, video content, …
enterprises run their services in “cloud” (e.g., Amazon Web Services, Microsoft Azure)
rise of smartphones: more mobile than fixed devices on Internet (2017)
~18B devices attached to Internet (2017)
2005-present: scale, SDN, mobility, cloud

## Slide 84: Summary
We’ve covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, access network, core
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
layering, service models
security
history
You now have:
context, overview, vocabulary, “feel” of networking
more depth, detail, and fun to follow!

## Slide 85: Additional slides

## Slide 86: ISO/OSI reference model
Two layers not found in Internet protocol stack!
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical
The seven layer OSI/ISO
reference model

## Slide 87: Wireshark
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Physical
application
(www browser,
email client)
application
OS
packet
capture
(pcap)
packet
analyzer
copy of all Ethernet frames sent/received

## Slide 88: Thanks